## Slide 1: BASIC ELECTRICAL & ELECTRONICS ENGINEERING

## Slide 2: Course Objectives:
To expose to the field of electrical & electronics engineering, laws and principles of electrical/electronic engineering and to acquire fundamental knowledge in the relevant field.

## Slide 3: Course Outcomes:
CO1: Extract electrical variables of AC & DC circuits using fundamental laws. (Understand)
CO2: Understand the operation of electrical machines and measuring instruments. (Understand)
CO3: Classify various energy resources, safety measures and interpret electricity bill generation in electrical systems. (Understand)

## Slide 4: PART A: BASIC ELECTRICAL ENGINEERING

## Slide 5: UNIT-I : DC & AC Circuits
DC Circuits: Electrical circuit elements (R, L and C), Ohm’s Law and its limitations, KVL, series, parallel, series-parallel circuits, Super Position theorem, Simple numerical problems.
AC Circuits: A.C. Fundamentals: Equation of AC Voltage and current, waveform, time-period,frequency, amplitude, phase, phase difference, average value, RMS value, form factor, peak factor, Voltage and current relationship with phasor diagrams in R, L, and C circuits, Conceptof Impedance, Active power, reactive power and apparent power, Concept of power factor (Simple Numerical problems).

## Slide 6
DC Circuits: Electrical circuit elements (R, L and C), Ohm’s Law and its limitations, KVL, series, parallel, series-parallel circuits, Super Position theorem, Simple numerical problems.

## Slide 12: CHARGE:
All materials are made up of one or more elements.
An element is a substance composed entirely of atoms of the same kind.
An atom consists of a massive core (nucleus) carrying protons and neutrons. Electrons move around nucleus in orbits at distances that are large as compared to the size of the nucleus.
Each electron has a mass of kg and a negative charge,
– e, equal coulomb.
Each proton carries a positive charge, e, equal in magnitude to that of an electron.
A neutron carries no charge and its mass is almost same as that of a proton.

## Slide 13
Under normal conditions, an atom is supposed to be electrically neutral.
The total positive charge on protons is equal to the total negative charge on electrons.
If an atom loses electron(s), it becomes positively charged. On the other hand, if an atom acquires excess electrons, it becomes negatively charged.
The charge is considered as the quantity of electricity.
The unit of charge is coulomb (C).

## Slide 15
The atoms in a metal (such as Cu, Al, etc.) are packed together to form a solid.
In such a case, the loosely bound electron in the outermost orbit is free to move from one atom to the other throughout the solid. Such electrons are called free electrons.
When a free electron moves, it carries a negative charge with it. Hence, the free electrons in a metal work as charge carriers.

## Slide 16: Drift Voltage:

## Slide 17: Electric Current:
Electric current is defined as rate of flow of positive charge.
The unit of current is ampere (A)
Types of Electric Current:
1)Uni-directional current ( Current flow always remains in one direction only)
2)Alternating Current (Current which keeps on reversing its direction continually)

## Slide 19
The current density in a conductor is the current per unit area of the cross section of the conductor.

## Slide 20: VOLTAGE OR POTENTIAL:

## Slide 21: POWER:
Horse power (hp) is also used as a unit of power [1 hp = 746 W].

## Slide 22: ENERGY:
Energy is capacity of doing work.
Energy = Work = Voltage *Charge = V * Q = V (It) = VIt = pt
Practical unit of electrical energy is kilowatt-hour(kWh).

## Slide 26: Types of Elements:
Active Elements (Element which supplies energy to a circuit)
Passive Elements (Element which can only receive energy, which it can either dissipate, absorb or store it in an electric field or a magnetic field)

## Slide 27: Active Elements
Voltage Source
Current Source

## Slide 56
Determine the equivalent inductance of the network shown below

## Slide 57
Calculate equivalent capacitance between terminals A & B

## Slide 58
Examine the power absorbed by each element in the circuit if X is a 13Ω resistor.

## Slide 59
Calculate the current delivered by the voltage source

## Slide 60
In circuit terminology, a loop is any closed path.
A mesh is a special loop, namely, the smallest loop one can have.
In other words, a mesh is a loop that contains no other loops.

## Slide 63
This theorem states that the response in a linear circuit at any point due to multiple sources can be calculated by summing the effects of each source considered separately, all other sources being made inoperative (or turned OFF).
The theorem is applicable only to a linear network (containing independent and/or dependent sources).

## Slide 66
Calculate the current through 8Ω resister using superposition theorem

## Slide 67
AC Circuits: A.C. Fundamentals: Equation of AC Voltage and current, waveform, time-period,frequency, amplitude, phase, phase difference, average value, RMS value, form factor, peak factor, Voltage and current relationship with phasor diagrams in R, L, and C circuits, Concept of Impedance, Active power, reactive power and apparent power, Concept of power factor (Simple Numerical problems).

## Slide 68: AC Circuits
Today, the vast majority of electrical power is generated, distributed, and consumed in the form of ac power.
The term ‘ac’ means ‘alternating current’. Such a current reverses its direction periodically.
In ac power, the voltages and currents vary with time sinusoidally.

## Slide 70
The frequency of ac supply in India is 50 Hz, which corresponds to time period, T = 1/50 = 0.02 s or 20 ms.
In USA, the frequency of ac supply is 60 Hz.

## Slide 91: Types of Power
Active Power (or) Real Power (or) Average Power
Reactive Power
Apparent Power

## Slide 92: i) REAL POWER/TRUE POWER/ACTIVE POWER/USEFUL POWER (P):
The power which is actually consumed or utilized in an AC Circuit is called True power or Active Power or real power.
The unit of Active or Real power is Watt.

## Slide 93: ii) REACTIVE POWER/USELESS POWER/WATT LESS POWER (Q):
The powers that continuously bounce back and forth between source and load is known as reactive Power (Q).
The unit of reactive power is Volt-Ampere reactive i.e. VAR

## Slide 94: iii) APPARENT POWER/COMPLEX POWER (S):
The combination of reactive power and true power is called apparent power.
The unit of Apparent power (S) : VA

## Slide 120: Numerical Problems